## Slide 1: Effect of Local Weather Conditions on Sky Brightness
Vayujeet Gokhale, David Caples, Jordan Goins, Ashley Herdman, James Tompkins & Emily Wren
Truman State University & Moberly Area Community College
MARAC Conference 2019
The thing’s hollow. It goes on forever, and. oh my God.
It’s full of stars!

## Slide 2: Talk Outline
Light Pollution
Truman State Observatory
  Telescope and dome
  Weather station
  Cloud Sensor
  All sky-camera
  Unihedron Light Sensors
Weather & Sky Brightness

## Slide 3: What is Light Pollution?
It is wasted light that performs no function or task
  Sky glow
  Glare
It is artificial light that goes where it’s not supposed to go
  Neighbor’s window (Light Trespass/clutter)
  Into the sky
Light Pollution is the introduction of artificial light, either directly or indirectly, into the natural environment.

## Slide 4: The Light Pollution Project
Research: Quantifying Light Pollution
  Quantify Sky brightness (Ongoing)
  DSLR Photometry (?)
  DSLR Photography (Ongoing)
Actions: Fixing the Problem
  Remedies for ‘bad’ light fixtures (Ongoing)
  Communicate with administrators (Done, and continuing)
  Funding Sources (MOSGC, Internal Truman funds)
Education & Outreach
  ‘Losing the Dark’ Planetarium Show, IDA brochures
  Astronomy Lab on light pollution
  Interdisciplinary research projects & Civic Engagement

## Slide 5
Flagstaff, Az 5 minute exposure, tracking ‘on’
Kirksville, Mo 1 minute exposure, tracking ‘on’

## Slide 6
Kirksville, Mo 15 minute exposure, tracking ‘off’
Flagstaff, Az 30 minute exposure, tracking ‘off’

## Slide 7: The Truman State Observatory
  CDK17 Planewave Telescope
  SBIG Aluma 814 & STT-8300 CCD cameras with standard Johnson B,V,R filters
  Fully Automated ObservaDome
  ACP, TheSky, and Maximdl6 control the observatory, telescope mount, and the CCD camera + guider
  Weather Station + Cloud Sensor interfaced with observatory control software

## Slide 8: The Weather Station
Davis Instruments 6152 ($750)
  Temperature, Humidity, Wind, and Rain sensors
  “Talks” wirelessly to observatory control software and overrides “human” commands in case of bad weather
Solar panel
Rain Sensor

## Slide 9: pion.truman.edu (Web interface)

## Slide 10: AAG Cloud Sensor ($350)

## Slide 11: All Sky Camera + Rasp-pi ($150+$100)

## Slide 12: Light Sensors: Sky Quality Meters
SQM (84o) and SQM-L (20o)
Readings in mag/arcsecond2
Higher reading = darker skies

## Slide 13: Sky Brightness Measurements
Weather-casing
Rasp-pi
Clamp
Two Types of Installations
“Automatic”: Battery Operated, data retrieval manual (no power supply)
Rasp-Pi Operated: Power supply needed, but data transfer via wireless internet

## Slide 14: Location: Magruder Roof & TSO

## Slide 15: Sky Brightness Measurements
Chart: Sky Brightness Comparison -- Different locations, Multiple Sensors
Stadium Lights?

## Slide 16: Sky Brightness Measurements
Chart: 01/07/2019 (t = 0@4:45PM)
8:00 PM
10:00 PM
3:00 AM

## Slide 17: Sky Brightness Measurements
Chart: 01/08/2019(t = 0@4:30PM)
8:00 PM
10:00 PM
3:00 AM

## Slide 18: Sky Brightness Measurements
Chart: 01/09/2019 (t = 0@4:30PM)
8:00 PM
10:00 PM
3:00 AM

## Slide 19: Results and Discussion
The SQM is a easy-to-use and reliable measure of the sky-brightness in semi-rural and urban locations (consistent results obtained over several months of observing).
Cloud cover seems to affect the sky brightness significantly.
We are still investigating the differences in sky brightness as a function of different kinds of clouds: cirrus, stratus, cumulus, etc.
We are also investigating the effect of other weather parameters such as rain, humidity and temperature (preliminary results suggest no obvious correlation).

## Slide 20: What can I do?
Repeat observations at locations with varying levels of light pollution to establish correlations between sky brightness and local weather conditions
  For example, does cloud cover in dark sky locations not affect sky brightness as much as it does in ‘bright-sky locations’?
Future Work

## Slide 21: What can I do?
We are looking for collaborators to set up light sensors on campuses to monitor light pollution, and testing the light sensors.
We are installing light shields and changing outdoor lighting color, and will report back what effect these actions have on the sky brightness in Kirksville.
Convince authorities to install smarter lights and retrofit older fixtures with dark-sky shields.
Convince more professional and amateur astronomers to take the lead in this effort before we lose the night sky altogether!
Future Work

## Slide 22: Installing Light Shields & ‘Warmer’ Color Lights

## Slide 23: Installing Light Shields & ‘Warmer’ Color Lights

## Slide 24: What can I do?
As astronomers, we have to act to stem the growing nuisance of light pollution.
  The problem is going to get worse with the growing use of LED lights.
  Be proactive about knowing what your school or city is planning in terms of outdoor lighting
    Usually, administrators are receptive to our concerns, but tend to be ignorant about issues such as light pollution
    Talking to them in time, will have positive impact with favorable outcomes
  Urge your graduate and undergraduate students to bring up and pursue this issue through student environmental groups and student government.

## Slide 25: References & Sources gokhale@truman.edu
IDA website: http://www.darksky.org/
Losing the dark sky movie: http://www.darksky.org/night-sky-conservation/290
Light Sensor: http://unihedron.com/projects/darksky/index.php
What happened to the Milky Way? http://www.theatlantic.com/video/index/384755/the-night-sky/
Paul Bogard: ‘The End of Night’ (Book) http://www.theatlantic.com/technology/archive/2013/07/let-there-be-night/278070/
Flagstaff Dark Skies: http://www.flagstaffdarkskies.org/
National Parks Service: http://www.nature.nps.gov/night/index.cfm

## Slide 26
Extra Slides

## Slide 27: Light Pollution
NASA/National Geographic

## Slide 28: Light Pollution Map
http://www.cleardarksky.com/

## Slide 29
Light Pollution is a LOCAL problem with LOCAL solutions

## Slide 30: Dark Sky Location: Anderson Mesa
Anderson Mesa

## Slide 31: Light Sensor: Set up
The entire set-up cost is less than $400 (for ethernet-sensor)

## Slide 32: Sky Brightness with Angle
Chart: 03/29/2016 - Truman State Observatory (Semi-Rural)
| 90 | 75 | 60 | 45 | 30 | 15 | 0
North | 20.14 | 19.916 | 19.796 | 19.64 | 19.554 | 19.65 | 19.872
East | 20.21 | 19.958 | 19.658 | 19.454 | 19.29 | 19.094 | 19.218
South | 20.14 | 20.242 | 20.198 | 20.05 | 20.002 | 20.088 | 20.182
West | 20.234 | 20.34 | 20.388 | 20.424 | 20.532 | 20.714 | 20.902
Horizon
Zenith
mags/arcsec2

## Slide 33: Sky Brightness with Angle
Horizon
Zenith
mags/arcsec2
Chart: 07/20/2017 - Truman State Observatory (Semi-Rural)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
North | 19.526 | 19.324 | 19.304 | 19.39 | 19.34 | 19.56 | 19.818 | 20 | 20.112 | 20.246
East | 19.192 | 19.204 | 19.05 | 19.186 | 19.26 | 19.458 | 19.702 | 19.93 | 20.156 | 20.19
South | 20.586 | 20.494 | 20.42 | 20.374 | 20.296 | 20.326 | 20.324 | 20.33 | 20.33 | 20.276
West | 20.374 | 21 | 20.748 | 20.73 | 20.612 | 20.552 | 20.542 | 20.52 | 20.402 | 21.144

## Slide 34: Sky Brightness with Angle
Chart: 04/02/2016 - Magruder Roof (City)
| 0 | 15 | 30 | 45 | 60 | 75 | 90
North | 16.706 | 16.668 | 16.87 | 17.266 | 17.986 | 18.42 | 18.6
East | 13.642 | 13.748 | 14.212 | 14.79 | 16.214 | 19.05 | 19.186
South | 14.888 | 14.958 | 15.642 | 16.298 | 17.47 | 18.752 | 18.994
West | 15.356 | 15.334 | 15.48 | 16.182 | 17.458 | 18.484 | 18.614
Horizon
Zenith
mags/arcsec2

## Slide 35: Sky Brightness with Angle
Horizon
Zenith
mags/arcsec2
Chart: 07/23/2017 - Magruder Roof (City)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
North | 15.928 | 16.362 | 16.776 | 17.28 | 17.524 | 17.72 | 18.418 | 18.648 | 18.736 | 18.742
East | 16.57 | 16.25 | 16.376 | 16.576 | 16.556 | 17.336 | 18.282 | 18.642 | 18.976 | 18.874
South | 17.398 | 16.658 | 16.69 | 16.786 | 16.974 | 17.508 | 18.442 | 18.738 | 18.83 | 18.894
West | 14.406 | 14.55 | 14.76 | 15.1 | 15.912 | 17.63 | 18.37 | 18.844 | 18.94 | 18.886

## Slide 36: Sky Brightness with Angle
Chart: 03/10/2016 – Lowell, Observatory, Anderson Mesa (15 miles SE of Flagstaff)
| 90 | 70 | 50 | 30 | 0
East | 21.422 | 21.528 | 21.648 | 21.918 | 22.424
West | 21.426 | 21.198 | 21.246 | 21.518 | 22.004
NW | 21.252 | 20.766 | 20.672 | 20.942 | 21.494
Horizon
Zenith
mags/arcsec2

## Slide 37: Sky Brightness with Angle
Horizon
Zenith
mags/arcsec2
Chart: 05/24/2017 – Lowell Observatory, Anderson Mesa
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
N | 22.206 | 21.96 | 21.81 | 21.722 | 21.694 | 21.722 | 21.796 | 21.88 | 21.87 | 21.89
W | 21.96 | 21.834 | 21.692 | 21.626 | 21.578 | 21.654 | 21.72 | 21.814 | 21.85 | 21.888
S | 22.404 | 22.132 | 21.984 | 21.836 | 21.782 | 21.72 | 21.756 | 21.816 | 21.854 | 21.9
E | 22.26 | 22.032 | 21.85 | 21.742 | 21.742 | 21.692 | 21.744 | 21.788 | 21.866 | 21.888

## Slide 38: Sky Brightness with Angle
Horizon
Zenith
mags/arcsec2
Chart: 03/29/2016 - Truman State Observatory (Semi-Rural)
| 90 | 75 | 60 | 45 | 30 | 15 | 0
North | 20.14 | 19.916 | 19.796 | 19.64 | 19.554 | 19.65 | 19.872
East | 20.21 | 19.958 | 19.658 | 19.454 | 19.29 | 19.094 | 19.218
South | 20.14 | 20.242 | 20.198 | 20.05 | 20.002 | 20.088 | 20.182
West | 20.234 | 20.34 | 20.388 | 20.424 | 20.532 | 20.714 | 20.902

## Slide 39: Continuous Sky Brightness Readings
mags/arcsec2
Chart: 03/13/2018 -- Lowell Observatory, Anderson Mesa
time

## Slide 40: Continuous Sky Brightness Readings
mags/arcsec2
Chart: 03/14/2018 -- Lowell Observatory, Anderson Mesa
time

## Slide 41: Continuous Sky Brightness Readings
mags/arcsec2
Chart: 04/08/2018 – Truman Observatory, Kirksville
Same Sensors as previous slide (3)
Older Sensors (2)
time
Not sure why there seems to be an offset – requires investigation

## Slide 42: Continuous Sky Brightness Readings Kirksville
mags/arcsec2
time
Chart: 
TSO
Magruder Hall

## Slide 43: Light Pollution Mitigation
Use low Temperature (T = 3000K) lights
Retrofit ‘dark sky friendly’ shields on ‘unfriendly’ fixtures
Contacting power companies and local administrators to ensure new fixtures are ‘dark sky friendly’
darksky.org

## Slide 44: Testing Light Shields

## Slide 45: Testing Light Shields
Testing done in Del and Norma Robison Planetarium at Truman

## Slide 46: Good and Bad Lighting: Typical Parking lot
Shaming the Admins
Students: You pay for this!

## Slide 47
Good
Bad
Notice the light going into the windows in the dorm rooms: Franklin Street

## Slide 48: Glare Bombs Galore: Franklin Street

## Slide 49: Glare Bombs Galore: Magruder/Violette Parking Lot

## Slide 50: Back of Envelope $$ Estimate
A single 100 W bulb costs about $25 to run for 12 hours a day for 365 days a year (@$0.12 per kW-hour).
If approximately 30% of light on average is ‘useless light’, this amounts of about $15 wasted per 100W light bulb.
Assuming 10,000 light fixtures (homes, apt complexes, street lights, gas stations, parking lots, offices, University etc) that are ‘on’ all night; this amounts to $150,000 wasted dollars per year.
And there is additional wastage from excessive indoor lighting as well.
Add to this the environmental impact, and secondary expenses related to health.

## Slide 51: Back of Envelope Carbon Footprint Estimate
1 KW-hour corresponds to 10,768 BTU.
4.4 x 106 KW-hour per year is consumed by ten-thousand 50 W bulbs burning 12 hours a day.
This corresponds to 4.74 x 1010 BTUs, which in turn corresponds to 2370 tons of coal, or 8170 barrels of oil.
If 30% of this is wasted as glare or sky-glow; this corresponds to about 700 tons of coal, or 2500 barrels of oil per year.

## Slide 52: What can I do?
http://www.darksky.org/assets/documents/PG3-residential-lighting.pdf

## Slide 53: Consequences of Light Pollution
Unshielded light sources
  Waste energy
    As much as 30% of outdoor lighting is beamed upward, toward the sky, rather than toward the ground.
  Are unsafe (very counterintuitive)
    Glare from misdirected bright lights can blind you.
    The human eye is a remarkable instrument capable of seeing very faint objects.
    However, if the brightness ratio between two objects is greater than 20:1; the eye cannot discern objects around the glaring light, rendering us vulnerable to an ambush.

## Slide 54: Non-shielded lights are unsafe
The glaring lamp to the right of the path was installed to protect. students at night.
Notes: Here is an excellent example of a poorly designed lighting scheme and how it does not contribute to campus safety. Notice the glare in the trees? Well the students don’t walk there, but on the ground where they do walk there are lots of shadows.

## Slide 55: Where did the student go?
Notes: Can you detect where the student is now? This light was meant to make the campus safer, but the lighting has only made the shadows easier to hide in. The student is now directly under the lamp, great place for a shadow isn’t it. Now we have created the shadows in which to lurk.

## Slide 56: Examples of Bad Lighting

## Slide 57: Examples of Bad Lighting

## Slide 58: Light Pollution
Unshielded light sources
  Negatively impact animals, including humans.
    Disturbs Circadian rhythm, resulting in insomnia, depression, cancer and cardio-vascular disease.
    The ‘blue’ portion of light is especially harmful since exposure to it affects release of the hormone Melatonin.
    In 2009, the AMA adopted resolutions that support reduction of light pollution and glare; and advocate for energy efficient, fully shielded outdoor lighting.

## Slide 59: Light Pollution
Unshielded light sources
  Negatively impact animals, including humans.
    100 million birds a year throughout North America die in collisions with lighted buildings and towers.
    Artificial lights can also cause migrating birds to wander off course and never reach their natural destination.

## Slide 60: Light Pollution
Unshielded light sources
  Negatively impact astronomy
    In astronomy, the role of ‘experimentation’ is largely taken by ‘observations’.
    These observations are based on light (gamma rays, x-rays, uv, visible, IR, Radio etc) emitted by objects at immense distances from Earth.

## Slide 61: Light Pollution
Unshielded light sources
  Negatively impact astronomy
    It is on the basis of studying the properties of this light that astronomers are able to piece together what the properties of the emitting object are.
    Sky glow interferes with astronomers’ ability to look the quality and quantity of light coming from these objects.
    Sky glow decreases the ability to see fainter stars, meteor showers and nebulae; and thus affects stargazing and amateur astronomy.

## Slide 62: What can I do?
Pima County, which includes Tucson, has the following ‘light ordinance’ in effect: The purpose of this code is to preserve the relationship of the residents of the City of Tucson, Arizona and Pima County, Arizona to their unique desert environment through protection of access to the dark night sky. Intended outcomes include continuing support of astronomical activity and minimizing wasted energy, while not compromising the safety, security, and well being of persons engaged in outdoor night time activities. It is the intent of this code to control the obtrusive aspects of excessive and careless outdoor lighting usage while preserving, protecting, and enhancing the lawful nighttime use and enjoyment of any and all property. It is recognized that developed portions of properties may be required to be unlit, covered, or have reduced lighting levels in order to allow enough lumens in the lighted areas to achieve light levels in accordance with nationally recognized recommended practices.
http://webcms.pima.gov/UserFiles/Servers/Server_6/File/Government/Development%20Services/Building/OLC.pdf